EQMOD protocol
Alain Klotz 2013 April 11th

This document has been written following a reverse engineering procedure using a serial port sniffer. There is no warranty about the security of the hardware. Be careful.
# 1. Open and configure communication port
Open the serial port and configure it with 9600 bauds, no parity, 8 data bits, 1 stop bit.
# 2. Sending message syntax
General syntax is ASCII characters terminated by a \r

The grammar follows the rules:
- The first character is one : to indicate the start of a command.
- The command is
- one letter (case sensitive) followed by
- 1 (hour angle motor) or by 2 (declination motor) followed eventually by
- a digital code (digit series or hexadecimal codes)

- Example 1: :a1 stands for command a for the hour angle motor.
- Example 2: :g210 stands for command g for the declination motor. Digital series is 10.
- Example 3: :H295EC42 stands for command H for the declination motor. Hexadecimal code is 95EC42 which corresponds to the decimal 4385941.
# 3. Receiving message syntax
The waiting time before reading the answer of a command is typically about 30 ms.

General syntax is ASCII characters terminated by a \r

Some commands have no response, other answers are a digital code (binary of hexadecimal).
# 4. Description of the motors and coding
The motors are of step by step type. For each axis, there is a worm that is linked to a teeth wheel. The coding seems to be done by the microstep counter. It is a relative encoder. When someone switch on the power of the mount, the encoder position is equal to decimal=-8388608 microsteps (hexadecimal=000080). See section 6.1 for the initialization.

The axis coding is of type apparent "hour angle" or "declination". The conversion from right ascension to hour angle must be done by the computer.

The hexadecimal to decimal conversion can be done using the Tcl proc:

proc eqmod_decode {s} {
   return [ expr int(0x[ string range $s 4 5 ][ string range $s 2 3 ][ string range $s 0 1 ]00) / 256 ]
}

The decimal to hexadecimal conversion can be done using the Tcl proc:

proc eqmod_encode {int} {
   set s [ string range [ format %08X $int ] 2 end ]
   return [ string range $s 4 5 ][ string range $s 2 3 ][ string range $s 0 1 ]
}

  Hexa Decimal
FFFF7F 8388607 (maximum)
000100 256
100000 16
0F0000 15
010000 1
000000 0
FFFFFF -1
F1FFFF -15
F0FFFF -16
00FFFF -256
000080 -8388608 (minimum)

The amplitude of microsteps coding is 16777216.

One 360° turn around a given axis correspond typically to 9024000 microsteps which is 53% of the microstep coding amplitude.

# 5. List of commands
One motor control is defined by its position and its speed. The position is given in microsteps units. The command (a) returns the number of microsteps to do one complete turn around the given axis (360° on the sky). The speed is given in microsteps/second units. The command (i) returns the next speed which will be set.

To obtain (i) from the tracking speed (speedtrack) expressed in degree/second, use the equation:

Slow speed case: (i) = (b) / speedtrack(deg/s) / (a) * 360
Fast speed case: (i) = (g) * (b) / speedtrack(deg/s) / (a) * 360

(b) is called the velocity parameter. The switch between slow and fast speed cases is done using the command :G. (see the example in the section 6.3).

The following commands returns only information (=read only):

Command	Digital coding	Units	Comment about the returned values
a	hexadecimal	microsteps / 360°	Number of microsteps for one turn over the sky
b	hexadecimal	microsteps2 / sec	Velocity parameter / (i) = (1|g) * (b) / speedtrack(deg/s) / ((a)/360)
c	hexadecimal	microsteps ?	unidentified parameter
d	hexadecimal	microsteps	initial position (j) when the mount is just switched on
e	hexadecimal	microsteps ?	unidentified parameter
f	3 digits	none	Slewing state / Digit1 (jog_type): 0|1|2|3|5|7=jog_slow+|stop+|jog_slow-|stop-|jog_fast+|jog_fast- / Digit2 (jog_state) : 0|1=Stopped|Jogging / Digit3: 0|1=PB?|OK?
g	hexadecimal	none	Fast tracking speed multiplier (set with :Gm3...)
h	hexadecimal	microsteps	Next position to reach
i	hexadecimal	none	Next tracking speed (set with :I, start with :J)
j	hexadecimal	microsteps	Current encoder position (set with :E)
k			unidentified parameter
l			unidentified parameter
m	hexadecimal	microsteps	start braking position with GOTO (set with :M)
n			unidentified parameter
o			unidentified parameter
p			unidentified parameter
q			unidentified parameter
r			unidentified parameter
s	hexadecimal	microsteps	Microsteps to a complete turnover of worm

For an EQ6 mount, the typical values are:

(a1)=9024000
(a2)=9024000
(b1)=64935
(b2)=64935
(d1)=-8388608
(d2)=-8388608
(e1)=1026
(e2)=1026
(g1)=16
(g2)=16
(s1)=50133
(s2)=50133

For a HEQ5 Pro mount, the typical values are:

(a1)=9024000
(a2)=9024000
(b1)=64935
(b2)=64935
(d1)=-8388608
(d2)=-8388608
(e1)=67585
(e2)=67585
(g1)=16
(g2)=16
(s1)=66844
(s2)=66844

Next examples are done using an EQ6 mount.

The following commands set values in the mount controller:

Command	Digital coding	Units	Comment about the input values
E	hexadecimal	microsteps	Set the relative encoder of microsteps to the hexadecimal value. Useful to initialize the coders.
F			Switch on the power to the motor
G	2 digits		Digit1 (motion_type): 0|1|2|3=offset|slow infinite|offset|fast infinite / Digit2 (motion_sense) : 0|1=increasing|decreasing microsteps / NB: increasing is diurnal or toward north pole for north hemisphere.
H	hexadecimal	microsteps	Set the next position increment to reach. The motion itself will be triggered by the command :J
I	hexadecimal	none	Set the next drift speed
J			Start a jog (=start the motion = start GOTO)
K			Kill the motor to stop the motion or the drift
M	hexadecimal	microsteps	Next position to start to decelerate. This value is not mandatory.
P	1 digit		unidentified action

# 6. Example of commands
## 6.1. Initialize the mount

If we have let the mount hour angle to 0h (meridian), then :

Send ":E1000000" (set the current hour angle position)

If we have let the mount declination to +90° (north pole), then :

decimal = 90/360*(a2) = 90/360*9024000 = 2256000 decimal microsteps = 806C22 hexadecimal

Send ":E2806C22" (set the current declination position)
## 6.2. GOTO motion
We want to slew the mount to the position hour angle = 2h00m00s and declination +48°30'00" (apparent coordinates). First, convert the celestial coordinates to the corresponding decimal degrees:

2h00m00s = 30°
+48°30'00" = 48.5°

One must stop the motors before slewing (else the slewing does not occur !):
:K1 (stop the motor before slewing)
:K2 (stop the motor before slewing)

Ask for the current hour angle:
:j1 => (j1) = C0BC05 = 376000 = 15° (for example)

Compute the difference of hour angles:
dif = 30°-15° = 15° = 15/360*(a1) = 15/360*9024000 = 376000 decimal = C0BC05 hexadecimal

Set the slewing mode to an increasing offset:
:G100

Set the next offset to slew:
:H1C0BC05

Start slewing:
:J1

Ask for the current declination:
:j2 => (j2) = 80A714 = 1353600 = 54° (for example)

Compute the difference of hour angles:
dif = 48.5°-54° = -5.5° = 5.5/360*(a2) = 5.5/360*9024000 = 137867 decimal = 8B1A02 hexadecimal

Set the slewing mode to a decreasing offset:
:G201

Set the next offset to slew:
:H28B1A02

Start slewing:
:J2

The end of slewing is checked by the Digit2 of :f1 and :f2
## 6.3. Diurnal motion drift
When a slewing is done, one must start the drift motion. It is defined as an infinite motion for the hour angle axis only. As a sideral day duration is 86164 seconds, the diurnal drift is 360./86164 = 0.0041781 °/second. A speed is defined as slow when it is lower than 0.25°/sec. A diurnal drift is a slow speed. We set the speed using the formula:

speed = (b1) / speedtrack(deg/s) / (a1) * 360 = 64935 / 0.0041781 / 9024000 * 360 = 620 decimal = 6C0200 hexadecimal

One must stop the motors before the jog (else the jog does not occur !):
:K1 (stop the motor before joging)

Set the slewing mode to an increasing infinite motion:
:G110

Set the diurnal speed of the hour angle axis:
:I16C0200

Start the drift motion:
:J1

To stop the motion, call :K1 then check the Digit2 of :f1to detect the end of deceleration. No new drift value can be send to the mount if the Digit2 is not equal to zero. This is important to program virtual pad buttons.
## 6.4. Artificial satellite motion drift
In case of a whatever motion one must distinguish the slow and the fast drift. A slow drift is limited to the upper limit of 0.25°/sec which is speed=10 decimal. The less the speed value is, the more the drift is. A speed<10 makes a lot of noise. Then, for drifts upper than 0.25°/sec one must use the fast drift mode. However, a strong noise occurs between 0.25°/sec and 1°/sec in the fast drift mode.

In this example, we want to drift the declination axis by -1.34°/sec.

We set the "fast" speed using the formula:

speed = (g2) * (b2) / speedtrack(deg/s) / (a2) * 360 = 16 * 64935 / 1.34 / 9024000 * 360 = 31 decimal = 1F0000 hexadecimal

Set the slewing mode to a decreasing fast infinite motion:
:G231

Set the speed of the declination axis:
:I21F0000

Start the drift motion:
:J2
# 7. Cables
The cable from PC to the mount consists to convert the RS232 levels down to lower levels, typically 5.0 Volts. Serial RS-232 communication (PC socket) works with voltages -15V to +15V for high and low. On the other hand, TTL logic (mount socket) operates between 0V and +5V:

RS-232	TTL	Logic
-15V … -3V	+2V … +5V	High
+3V … +15V	0V … +0.8V	Low

Thus the RS-232 signal levels are far too high TTL electronics, and the negative RS-232 voltage for high can’t be handled at all by computer logic. To receive serial data from an RS-232 interface the voltage has to be reduced. Also the low and high voltage level has to be inverted.

The EQMOD cable is based on a MAX232 from Maxim which in one package contains the necessary drivers and receivers to adapt the RS-232 signal voltage levels to TTL logic. It just needs one voltage (+5V or +3.3V) and generates the necessary RS-232 voltage levels.

Informations:
http://eq-mod.sourceforge.net/eqdirect2.htm

## 7.1. DB9 RS232 to DB9 TTL

## 7.2. DB9 TTL to RJ45
In case of HEQ5-Pro mounts, you need to convert the DB9 TTL outpout into a RJ45 socket:

Solder Pin 4 of the RJ45 to the Pin 5 of the TTL DB9 (GND)
Solder Pin 5 of the RJ45 to the Pin 2 of the TTL DB9 (RXD)
Solder Pin 6 of the RJ45 to the Pin 3 of the TTL DB9 (TXD)