Tcl programming to use the telescope driver libtelscript
Alain Klotz 2013 february 2

# 1. Introduction
Driving a telescope with AudeLA is based on a Tcl instantiation of an AudeLA object called tel1. The driver itself is written in C/C++ code (source codes in audela/src/libtel).

As a consequence, an astronomer interested to develop a new telescope driver for AudeLA must program the corresponding C/C++ code that is not easy for most astronomers. The libtelscript telescope library is a programmed C/C++ telescope driver for AudeLA that calls a Tcl script every few milliseconds. By this way it becomes possible to develop a Tcl script that can drive a telescope.
# 2. An example
The telscript_template_equatorial.tcl script simulates a basic equatorial telescope driver. To test this driver, type the following terminal command:

tel::create telscript -telname mytel -script $audace(rep_install)/gui/audace/plugin/mount/telscript/telscript_template_equatorial.tcl -home \{$audace(posobs,observateur,gps)\}

During the creation of tel1, firstly the script telscript_template_equatorial.tcl is sourced. This script must contains at less two procs: setup and loop (with no input parameters). Secondly, the proc setup is called. The contents of the setup proc should establish the physical connections with the telescope controller. Thirdly, the proc loop is called inside an infinite loop. The proc loop should contain the code to process the actions to drive the telescope. After the creation, the tel1 commands like "tel1 radec coord" and others can be used.
# 3. Variable exhange between C and Tcl

The Tcl array telscript is used to exchange data between the Tcl script and the C code of libtelscript. For this reason, don't forget to write global telscript as the first line of the procs of the script. Anyway, the variable telscript(def,telname) contains the name defined by the -telname option (=telscript_template_equatorial by default). Herafter we designed telname the value of telscript(def,telname).
## 3.1. From C to Tcl
Before calling the loop proc, the following variables are updated from tel1 functions:

- telscript($telname,action_next) can be equal to one of the following values: "motor_on" "motor_off" "motor_stop" "radec_init radec_goto" "hadec_init" "hadec_goto" "move_start". these values are automatically provided by "tel1 radec motor on|off" "tel1 radec stop" "tel1 radec init" "tel1 radec goto" "tel1 hadec init" "tel1 hadec goto" "tel1 radec move".
- telscript($telname,action_prev) = previous action before moving by the move or by a goto. See telscript($telname,action_next) for the values provided.
- telscript($telname,ha0) = Hour angle position to reach for the next GOTO or for the next MATCH. Provided by "tel1 hadec init" "tel1 hadec goto"
- telscript($telname,ra0) = Right Ascension position to reach for the next GOTO or for the next MATCH provided by "tel1 radec init" "tel1 radec goto".
- telscript($telname,dec0) = Declination position to reach for the next GOTO or for the next MATCH Provided by "tel1 radec init" "tel1 radec goto" "tel1 hadec init" "tel1 hadec goto"
- telscript($telname,radec_move_rate) = Speed (0 to 1) for moving. Provided by "tel1 radec move"
- telscript($telname,move_direction) = Direction (n,s,e,w) for moving. Provided by "tel1 radec move"
## 3.2. From Tcl to C
After calling the loop proc, the following variables are commited
to the C code to be used by tel1 functions:

- telscript($telname,coord_app_cod_deg_ra) = Current Right Ascension position. Used by "tel1 radec coord"
- telscript($telname,coord_app_cod_deg_dec) = Current Declination position. Used by "tel1 radec coord" "tel1 hadec coord"
- telscript($telname,coord_app_cod_deg_ha) = Current Hour angle position. Used by "tel1 hadec coord"
- telscript($telname,action_next): Any change of the value will be known at the the next loop.
- telscript($telname,action_prev)=telscript($telname,action_next): Allow to keep in memory the previous "next" action.
- telscript($telname,motion_next): A string that can be used to distinguish the action to do and the motion of the telescope.
- telscript($telname,motion_prev)=telscript($telname,motion_next)
- telscript($telname,message): Usefull to debug. Append strings to this variables in the proc loop can be read easilly by this way.

# 4. tel1 special functions
The following functions are usefull to check the states of the proc loop.

tel1 looperror. To read the errors found in the proc loop. A empty string is returned if there is no error.

- tel1 source. To source again the script (useful to correct the loop proc)
- tel1 variables: Return a list that contains the variables of the array telscript. A good way to display the exchange variables is to type:

foreach res [lsort [tel1 variables]] { console::affiche_resultat "$res\n" }

- tel1 loopeval. To send a string to evaluate inside the proc loop. The result is displayed using "tel1 loopresult"
- tel1 loopresult. To display the result of "tel1 loopeval"
- tel1 action. To display the last action_next and the number of loops ever done.
# 5. A simple script template
The following script is a template that initializes exchange variables. This ca, be completed to adapt it to any telescope driver.

# --- common defined variables
# telscript(def,telname) is ever defined before the source of this script
set telscript(def,speed_diurnal) [expr 360./(23*3600+56*60+4)] ; # diurnal motion (deg/sec)

# === Proc called one time at the start of the driver
proc setup { } {
  global telscript
  # --- Get useful variables
  set telname $telscript(def,telname)
  # --- The initial telescope position is HA=0 et Dec=0
  set telscript($telname,coord_app_cod_deg_ha) 0
  set telscript($telname,coord_app_cod_deg_dec) 0
  set telscript($telname,jdutc_app_cod) [mc_date2jd now]
  # --- The initial telescope motion is "motor off"
  set telscript($telname,speed_app_cod_deg_ha) 0
  set telscript($telname,speed_app_cod_deg_dec) 0
  set telscript($telname,motion_next) "stopped"
  # --- Set a comment that the setup is OK
  set telscript($telname,status) "setup OK"
  #catch {set f [open "log.txt" w] ; close $f}
}
# === Proc called on loop after the start of the driver
proc loop { } {
  global telscript
  # --- Get useful variables
  set telname $telscript(def,telname)
  set home $telscript($telname,home)
  set telscript($telname,message) ""
  # === Compute current apparent coordinates for "tel1 radec coord"
  # --- variables used to commit "tel1 radec coord" and "tel1 hadec coord" after this proc
  set telscript($telname,coord_app_cod_deg_ha) $ha
  set telscript($telname,coord_app_cod_deg_dec) $dec
  set telscript($telname,coord_app_cod_deg_ra) $ra
  # === Process actions (actions are set by tel1 commands)
  if {$telscript($telname,action_next)=="motor_on"} {
     # --- Action = motor_on
     # (don't change telscript($telname,motion_next))
  } elseif {$telscript($telname,action_next)=="motor_off"} {
     # --- Action = motor_off
      # (don't change telscript($telname,motion_next))
  } elseif {$telscript($telname,action_next)=="motor_stop"} {
     # --- Action = motor_stop
     set direction [string toupper $telscript($telname,move_direction)]
  } elseif {$telscript($telname,action_next)=="radec_init"} {
     # --- Action = radec_init
     set telscript($telname,coord_app_cod_deg_ra) $telscript($telname,ra0)
     set telscript($telname,coord_app_cod_deg_dec) $telscript($telname,dec0)
  } elseif {$telscript($telname,action_next)=="radec_goto"} {
     # --- Action = radec_goto
     set ra0 $telscript($telname,ra0)
     set dec0 $telscript($telname,dec0)
  } elseif {$telscript($telname,action_next)=="hadec_init"} {
     # --- Action = radec_init
     set telscript($telname,coord_app_cod_deg_ha) $telscript($telname,ha0)
     set telscript($telname,coord_app_cod_deg_dec) $telscript($telname,dec0)
  } elseif {$telscript($telname,action_next)=="hadec_goto"} {
     # --- Action = hadec_goto
     set ha0 $telscript($telname,ha0)
     set dec0 $telscript($telname,dec0)
  } elseif {$telscript($telname,action_next)=="move_start"} {
     # --- Action = move_start
     set rate $telscript($telname,radec_move_rate)
     set direction [string toupper $telscript($telname,move_direction)]
  }
  # --- Set a comment that the loop is OK
  set telscript($telname,status) "loop OK"
}